## Slide 1: Advanced Reliability and Safety Analysis
RAVEN Workshop

## Slide 2: Outline
Dynamic Probabilistic Risk/Safety Analysis
  Classic vs. Dynamic PRA
Adaptive Sampling
  Limit Surface

## Slide 3: Reliability and Safety Analysis
Safety Analysis: determine the likelihood a system will not perform its functions in a specified time period
Reliability Analysis: determine the ability of a system to perform its functions in a specified time period

## Slide 4: Dynamic Probabilistic Risk/Safety Analysis
Classic Probabilistic Risk/Safety Analysis
  Static boolean logic structures
    Event-Trees / Fault-Trees
  Accident sequence set by the analyst
  Timing of events partially considered
Dynamic Probabilistic Risk/Safety Analysis
  Direct use of system simulation codes
  Coupled with stochastic analysis tools (e.g., RAVEN)
  Accident sequence set by the system control logic
  Timing of events fully considered

## Slide 5: Dynamic Probabilistic Risk/Safety Analysis
Stochastic analysis
Sample the pdfs
Run N times system simulation code(s)
Evaluate desired FOMs
Deterministic modeling
Plant modeling
External event modeling
Stochastic modeling
Identify uncertain parameters and associate a pdf

## Slide 6: ROMs: Classifiers
ROMs as mathematical models designed approximate an input-output relationship
Classifiers: output variable is boolean
  i.e., 0 or 1
  e.g., OK or Failure

## Slide 7: Adaptive Sampling
Computational costs might be impractical
  Computationally expensive codes
  Many simulation runs are often required
Reduced Order Modeling can be a solution
  Objective: reduce the complexity of the problem
Search of the limit surface: boundaries in the input space between failure and success
Ω

## Slide 8
Reliability Analysis: Limit Surface Search
Train a surrogate model
Use the surrogate model to determine an approximation of the limit surface
Choose a set of samples on the approximated limit surface
Run the “real” model to verify the approximation
Generate a set of training simulations to sample the plant response
Reach convergence
No
Yes
Stop

## Slide 9: Failure Probability Calculation From LS
Limit surface has a pure deterministic information
Probabilistic information is contained in the integral within the limit surface weighted by the set of distributions
For a new set of distributions the integral needs to be recalculated but the limit surface is unchanged
Ω

## Slide 10: Advanced Reliability and Safety Analysis: Hands on
RAVEN Workshop

## Slide 11: Objectives
Run and Write your first reliability analysis input file
Understand how RAVEN performs reliability analysis using the LimitSurfaceSearch Sampler
Perform the adaptive sampling
Compute the probability of failure

## Slide 12: Getting on the same page
This workshop will include interactive examples
paths given starting at raven (raven/)
Slides are provided as well:
~> cd projects/raven
~/projects/raven> git checkout workshop_2018
~/projects/raven> git pull
raven/doc/workshop/advancedReliability

## Slide 13: Example Code
RAVEN samples codes
For experiment, we’ve provided some physics in a code
projectile.py
Given:
  , the initial vertical position
  , the initial horizontal position
  , the launch angle
  , the launch velocity
Calculates:
  , the horizontal position throughout the arc
  , the vertical position throughout the arc
  , the range or furthest point reached
  , the time of flight

## Slide 14: Exercises
4 exercises are proposed:
  Execute a Limit Surface search analysis on the projectile.py model
  Add a LimitSurfaceIntegral post processor to compute the failure probability
  Change the the ROM classifier to check how the limit surface changes
  Change the distributions in the LimitSurfaceIntegral to check how the failure probability changes

## Slide 15: Exercise 1: Reliability Analysis – Limit Surface Search

## Slide 16
Define the distributions:
  Weigh the error estimation
  Generate a probability-weighted metric for grid construction
  Determine the probability of being inside one of the regions identified by the limit surface
  Define the surrogate model (acceleration ROM) to be used for the adaptive sampler
Define the adaptive sampler:
  Convergence control and grid
  Import the acceleration ROM
  Associate the distribution with the variables
Define the adaptive sampling step
Reliability Analysis: Limit Surface Workflow

## Slide 17: Exercise 1: Reliability Analysis – Limit Surface
Input file name: 1_adaptive_sampling.xml
Distributions
<Models>
...
<ROM name=”acceleration_ROM" subType="SciKitLearn">
<Features>v0,angle</Features>
<Target>decision</Target>
<SKLtype>svm|SVC</SKLtype>
<kernel>rbf</kernel>
<gamma>10</gamma>
<C>50</C>
</ROM>
</Models>
Steps
Samplers
Models
Functions
DataObjects

## Slide 18: Exercise 1: Reliability Analysis – Limit Surface
Input file name: 1_adaptive_sampling.xml
Distributions
<Functions>
<External name=”adaptive_test_goal" file=”decision">
<variable>r</variable>
</External>
</Functions>
Steps
Samplers
Models
Functions
DataObjects
def __residuumSign(self):
if self.r >100.:
return -1
else:
return 1
File: adaptive_test_goal.py

## Slide 19: Exercise 1: Reliability Analysis – Limit Surface
Input file name: 1_adaptive_sampling.xml
Distributions
<Samplers>
...
<LimitSurfaceSearch name="Adaptive">
<ROM class="Models" type="ROM" >acceleration_ROM</ROM>
<Function class="Functions" type="External" >decision</Function>
<TargetEvaluation class="DataObjects" type="PointSet">results</TargetEvaluation>
<Convergence limit=”3000" forceIteration="False" weight=”CDF"
persistence=”20">1e-4</Convergence>
<variable name=”v0">
<distribution>vel_dist</distribution>
</variable>
<variable name=”angle">
<distribution>angle_dist</distribution>
</variable>
<constant name=”x0">0 </constant>
<constant name=”y0">0 </constant>
</LimitSurfaceSearch>
</Samplers>
Steps
Samplers
Models
Functions
DataObjects

## Slide 20: Exercise 1: Reliability Analysis – Limit Surface
Input file name: 1_adaptive_sampling.xml
Distributions
<Steps>
<MultiRun name=”adaptive_sampling" pauseAtEnd="True">
add the step on your own
</MultiRun>
</Steps>
Steps
Samplers
Models
Functions
DataObjects

## Slide 21: Exercise 2: Failure Probability Calculation from LS

## Slide 22: Exercise 2: Failure Probability Calculation From LS
Input file name: 2_ls_probability_computation.xml
Distributions
<Models>
…
<PostProcessor name="LS_Integral" subType="LimitSurfaceIntegral">
<tolerance>0.05</tolerance>
<seed> 02201986 </seed>
<outputName> EventProbability </ outputName >
<integralType>MonteCarlo</integralType>
<target>decision</target>
<variable name=”v0">
<distribution> vel_dist </distribution>
</variable>
<variable name=”angle">
<distribution> angle_dist </distribution>
</variable>
</PostProcessor>
…
</Models>
Steps
Samplers
Models
Databases
DataObjects

## Slide 23: Exercise 2: Failure Probability Calculation From LS
Input file name: 2_ls_probability_computation.xml
Distributions
<Steps>
<IOStep name=”load_ls">
<Input class=”Files" type="" >limitSurfaceFile</Input>
<Output class="DataObjects” type="PointSet" >limitSurface</Output>
</IOStep>
<PostProcess name="integral">
add the step on your own
</PostProcess>
</Steps>
Steps
Samplers
Models
Databases
DataObjects