## Slide 1: Time-Dependent Statistics
RAVEN Workshop

## Slide 2: Objectives
Explore HistorySets in RAVEN
Extend statistical analysis to a time-dependent case
Plot time-evolving statistics
Write a RAVEN input to accomplish a particular task

## Slide 3: Data Structures in RAVEN: Review
DataObjects
  The vehicle for data in RAVEN calculation flows
  Store each “realization” in a “row”
  In general, consider like a CSV
  Two main subtypes
PointSet
  Each entry is a single-valued entry (float, string, etc)
  If a vector is provided, keeps only the last entry
HistorySet
  Each input is a single-valued entry
  Outputs all share a single vector index (e.g. “time”)
  Index specified through pivotParameter

## Slide 4: Data Objects: Visualization
Point Set
y0 | ang | r | t | ProbWt | PtProb
0.0 | 5.0 | 15.95 | 0.5336 | 0.00028 | 0.0125
0.033 | 7.667 | 24.53 | 0.825 | 0.00056 | 0.0125
0.3 | 55.67 | 85.75 | 5.064 | 0.00056 | 0.0125
1.0 | 85.0 | 16.03 | 6.132 | 0.00028 | 0.0125
Inputs
Outputs
Metadata
Samples
(Runs)
Variables

## Slide 5: Data Objects: Visualization
History Set
y0 | ang | t | x | y | PtProb
0.0 | 5.0 | <vector> | <vector> | <vector> | 0.0125
0.033 | 7.667 | <vector> | <vector> | <vector> | 0.0125
Inputs
Outputs
Samples
(Runs)
Variables
Pivot
Metadata
t | x | y
0 | 0 | 0
0.1 | 0.02 | 0.1
0.2 | 0.04 | 0.19
0.3 | 0.06 | 0.27

## Slide 6: History Sets and Projectile
Projectile has 2 outputs we haven’t been using
  horizontal position over time
  vertical position over time
  both depend on “time” t
We were using “t” as “time of flight” before
  If a PointSet gets a vector, it takes the last entry
  Projectile calculated “t” for whole simulation
  RAVEN only kept last value of “t”

## Slide 7: Exercise 7
Producing Histories

## Slide 8: Extending Projectile to HistorySets
Start with copying simple PointSet sampling example
  Copy to 7_history_sets.xml
Change the output variables from “r, t” to “x, y, t”
  Models
  DataObjects
    Don’t change “placeholder”
    PointSet  HistorySet for “results”
    Outputs are x and y
    Pivot parameter is “t” (see user manual, section 12)
Run it! Look at the “to_file” outputs CSVs.
Extra credit: Try plotting “y” vs “t”!
raven/doc/workshop/forwardSampling/exercises/6_point_sets.xml

## Slide 9: Exercise 8
Synchronizing Histories

## Slide 10: History Synchronization
Histories not synchronized from “projectile” samples
  Difficult to perform analyses without synchronizing
Solution: HistorySetSync Interfaced PostProcessor!
  See section 15.5.10 and 15.5.10.4 in the manual
Try it out!
  Copy 7_history_sets.xml to 8_history_sync.xml
  Add HistorySetSync PostProcessor to Models
  Add PostProcessor step to Steps
  Add synced HistorySet to DataObjects
  Add new OutStream Print to print synced data

## Slide 11: Exercise 9
Time-Dependent Statistics

## Slide 12: Time-Dependent Statistics
What happens when you do statistics on HistorySet outputs?
  Time evolution of statistics
  Snapshot of statistics at each time
Try it out!
  Objective: create the following plots versus “time”
    v0, y0, angle average
    x-position, y-position average, variance
    sensitivity of y with respect to v0, y0, angle
    sensitivity of x with respect to v0, y0, angle
Use everything you’ve learned so far!
Don’t forget data must be synced before BasicStatistics is run!

## Slide 13: Bonus Exercises
So you think you’re RAVEN …

## Slide 14: Ideas
Try out an Optimizer
  Find the optimal y0, v0, angle to get maximum range
  Find the optimal y0, v0, angle to minimize time-of-flight